## Slide 1: A modern captain bed
Rémi Cura, 2015

## Slide 2: Introduction
Main design ideas
  A bed with massive storage space
  Tough
  Doable, can be assembled/disassembled
  Beautiful materials for a nautical style aesthetic

## Slide 3: Technical choices

## Slide 4: Esthetic choices
Main inspiration is actual captain bed, in particular for:
  Its compactness (nothing protruding)
  Its warm colors (mahogany+ brass)
  Its toughness
  Its simplicity (no curves)
We adapt it to modern constraints
  Maximal storing space
  A few sharp edges accepted
Height
  To limit the height impression, we use clear contrasted wood for vertical parts

## Slide 5: Technical choices
Passing through drawers (full bed width)
Main dimensions
  Mattress is 1600*2000mm
  Bed frame is at about height 850 mm
  Thickness for main parts (belt) :30mm
  Thickness structural part(frame) : 20 mm
  Thickness secondary element (drawer bottom): 10mm
Joinery choices
  removable
  Mecanically sound
  Easy to construct
  Use metal parts only when absolutely necessary

## Slide 6: Technical choices
About materials
  Visible wood:
    Hard, dark/red colour(acajou/sapelli/merisier/padouk)
  Structure (cloison):
    Hard, light colour: hêtre/chataignier/frêne
  Drawer Not visible:
    rigid cheap :plywood/latté
  Mattress floor:
    Light cheap(pin/epicea…)
hardware
  Visible : brass
  Invisible : brass/ stainless/ steel

## Slide 7: Technical choices
About sketchup 3D model
  More a detailed concept
  Joinery is sometime showed, but not always ( sketchup is buggy)
  Some stuff are hand placed and are not precise

## Slide 8: Global model visualisation

## Slide 9: Global visu

## Slide 10: Global visu

## Slide 11: Global visu
(all drawers and doors have handle)
(behing door, either a box, shelf, or nothing)

## Slide 12: Global visu
(all drawers and doors have handle)
(this illustration misses some part of the drawers supports)

## Slide 13: Global visu
(tous les tiroirs et portes devraient avoir une poignée)
(les assemblages des tiroirs ne sont pas montrés ici)
Note : les doubles portes battantes permettent d’accéder au même coffre.
Avec les tiroirs traversant, cela permet d’utiliser le stockage même quand le lit est le long d’un murs sur un des côtés.
Les doubles battants permettent un espace au pied du lit plus réduit, et sont meilleurs d’un point de vue macanique (800mm de portée un peu long pour un simple battant)

## Slide 14: Building step view

## Slide 15: Socle
(Not all joins are drawn)

## Slide 16: + cloisons
(Not all joins are drawn)

## Slide 17: + traverses
(Not all joins are drawn)

## Slide 18: + supports tiroirs
(Not all joins are drawn)

## Slide 19: + sommier
(Not all joins are drawn)

## Slide 20: Joinery details
Joins principles are shown, but not all joins.
Drawing every join in sketchup is a pain

## Slide 21: + socle
(Not all joins are drawn)
Dovetails on half width allow easy dissambly, are super rigid, and will handle dimension variations
Tenon are simple and save wood

## Slide 22: + cloisons
(Not all joins are drawn)
We use hardware to join panneaux. This allow to control tightness and is still easily removable.

## Slide 23: + ceinture
(Not all joins are drawn)
Il ne seemble pas y avoir bcp de possiblités pour ces assemblages car la largeur des planches (30mm) est insuffisante pour bcp d’assemblages plus solides.
Ces jonctions doivent être extremement fortes.
On utilise donc des vis traversantes cachées par des bouchons de bois pour l’esthétique

## Slide 24: + support tiroir
(tous les assemblages ne sont pas représentés)
Ces assemblages devrait être faisable avec une défonceuse avec meche droite assez fine et gabarit.
C’est essentiel car il y en a bcp.
L’onglet en basde l’assemblage permet de bien repartir la charge du tiroir
Les arondes permettent de transmettres les mouvements des cloisons à toute la structure

## Slide 25: + tiroir
Les clefs d’arondes sont représentées non coupées
L’assemblage par clef d’aronde semble etre un bon compromis d’usinage, puisqu’on fait d’abord un assemblage « facile» avec feuillures, puis on colle le tiroir.
On défonce les clefs sur le tiroir déjà assemblé, ce qui évite l’utilisation d’un gabarit à queue d’aronde.
Mécaniquement les clefs bloque traction et déformation par le poids
C’est esthétique si les clefs sont faites dans un autre bois
Elles ne sont pas débouchantes sur la facade
Le système de fixation facade tiroir est soit vis taraudé, soit aronde coulissante verticalement, ce qui ferait perdre bcp de bois

## Slide 26: Finish
  Matte varnish (watter)
  How to protect brass?
  Anti-vibration carpet (designed for wooden flor) to compensate ground height variation and increase friction?

## Slide 27: Optionnal

## Slide 28
Bonus:
A brass shelf.
Can be pushed inside
Can be used only fully in or fully out
Allow for a bedside table without blocking drawers opening
Joinery : groove; at the end, centering -45° + 45° profile.
Shelf surface is itched with acid, sculpted, or machined with cnc. Could also be sculpted leather.
Idea for patter : nautical map from 19th century, vintage moon map.